## Slide 1
Machine Learning for Network Telemetry
A Survey of Methods, Applications, and Emerging Trends
NET3006A — Network Management and Machine Learning
Carleton University | Winter 2026 | Dr. Jie Gao
Abdul Rehman | Esam Mukbil | Hashim Kshim | Mazen Alhassan
Option 1: Survey / Reading Project — Topic 2
Detect
Predict
Optimize
1 / 25

## Slide 2
Presentation Outline
Presenter: All Members
1.
Introduction & Motivation
Abdul Rehman
2.
What Network Telemetry Means
Abdul Rehman
3.
Why Machine Learning Helps
Esam Mukbil
4.
Anomaly Detection Methods
Esam Mukbil
5.
Main Lessons from Anomaly Detection
Mazen Alhassan
6.
Performance Prediction
Mazen Alhassan
7.
QoS Optimization
Hashim Kshim
8.
Main Lessons for Performance & QoS
Hashim Kshim
9.
Telemetry Pipeline
Mazen Alhassan
10.
Nokia Example
Mazen Alhassan
11.
Ericsson Example
Hashim Kshim
12.
Future Trends: 6G & GenAI
Hashim Kshim
13.
Open Challenges
Hashim Kshim
14.
Conclusion
Hashim Kshim
Abdul Rehman
Esam Mukbil
Mazen Alhassan
Hashim Kshim
2 / 25

## Slide 3
PART 1
Introduction & ML for Anomaly Detection
Presenter: Abdul Rehman
3 / 25

## Slide 4
What is Network Telemetry?
The network continuously reports what is happening inside it
Presenter: Abdul Rehman
It is the live data that routers, switches, and links send about their health and traffic.
It tells us things like delay, packet loss, throughput, CPU use, and errors.
Modern systems stream this data automatically instead of waiting for slow manual checks.
That gives operators a clearer and faster view of what the network is doing.
Telemetry is the input that ML uses to spot trouble and predict future problems.
Simple View
Devices
Data
ML
Examples of Telemetry Data
Flow data Packet traces Device metrics INT path details Logs and events
Presenter: Abdul Rehman
4 / 25

## Slide 5
From Traditional Monitoring to Streaming Telemetry
Why modern networks moved beyond slow polling and basic dashboards
Presenter: Abdul Rehman
Traditional Monitoring
Checks devices every so often Often slower and less detailed Problems may be noticed after users are affected Works poorly at modern network scale
Streaming Telemetry
Data is pushed continuously More detailed and more real-time Makes faster detection and response possible Better fit for ML and automation
Main Point
Better telemetry gives ML better input, and better input leads to better decisions.
Presenter: Abdul Rehman
5 / 25

## Slide 6
Where Telemetry Data Comes From
Different network signals combine to give a full picture
Presenter: Abdul Rehman
Devices
Routers, switches, and access points report health and counters.
Traffic Flows
Flow records show who is talking, how much, and how often.
Packets
Packet traces reveal detailed behavior on the wire.
Logs & Events
Logs capture warnings, failures, and configuration changes.
Why this matters
ML works best when it can learn from multiple types of telemetry instead of a single signal.
Presenter: Abdul Rehman
6 / 25

## Slide 7
Why Telemetry Matters in Modern Networks
Telemetry supports visibility, reliability, and automation
Presenter: Abdul Rehman
1
See problems earlier
Operators can notice trouble before outages spread.
2
Understand performance
Teams can measure delay, loss, and congestion more clearly.
3
Support automation
Telemetry gives ML the evidence it needs to recommend actions.
4
Scale to new networks
5G, cloud, and large systems need better visibility than old tools provide.
Simple Summary
Telemetry is the network's evidence. ML uses that evidence to find patterns, explain behavior, and support faster decisions.
Presenter: Abdul Rehman
7 / 25

## Slide 8
Why Apply ML to Network Telemetry?
The challenge is not collecting data. It is understanding it fast enough.
Presenter: Esam Mukbil
ML
Why use ML here?
Too much data
Large networks create huge telemetry streams every second.
Problems are hidden
Small clues across many signals are hard to notice manually.
Speed matters
Teams need answers before users feel the problem.
Networks change
Traffic and paths move, so fixed rules become outdated.
What We Cover
Anomalies | Prediction | QoS | Industry | Future trends
Presenter: Esam Mukbil
8 / 25

## Slide 9
ML Methods for Anomaly Detection
A visual summary of the main model families
Presenter: Esam Mukbil
Autoencoders
Learn what normal traffic looks like. If new data looks very different, it may be an anomaly.
Unsupervised
LSTM / GRU
Look at patterns over time. They help catch spikes, drops, or strange sequences in telemetry.
Deep Learning
Isolation Forest
Quickly separates unusual points from common ones. Useful when speed is important.
Unsupervised
One-Class SVM
Builds a boundary around normal behavior, then flags data outside that boundary.
Semi-supervised
GAN-based Models
Generate or compare normal-looking samples so unusual behavior stands out more clearly.
Generative
Presenter: Esam Mukbil
9 / 25

## Slide 10
Anomaly Detection: Main Lessons
Less text, stronger takeaways
Presenter: Mazen Alhassan
Deep learning is strong
Deep learning often beats older statistical methods when telemetry has many features.
Unsupervised is practical
Unsupervised learning is popular because real networks rarely have enough labeled anomaly data.
Hybrid models help
Hybrid models work well because they mix strong feature learning with fast scoring.
Speed is still hard
Real-time use is still hard because accurate models can be expensive to run at scale.
Key Takeaway
Best results often come from models that learn normal behavior first because labeled anomaly data is limited.
Presenter: Mazen Alhassan
10 / 25

## Slide 11
PART 2
Methods, Findings & Prediction
Presenters: Esam Mukbil & Mazen Alhassan
11 / 25

## Slide 12
ML for Network Performance Prediction
Using telemetry to estimate what the network will do next
Presenter: Mazen Alhassan
Time-Series Forecasting
• LSTM and GRU models learn how metrics change over time
• They forecast delay, jitter, loss, and throughput
• Useful when recent behavior helps predict the near future
Graph Neural Networks (GNNs)
• Represent the network as devices and links in a graph
• Good for path-based prediction because topology matters
• They capture how one congested link can affect other paths
Ensemble & Hybrid Methods
• Combine different models to improve robustness
• Often more accurate than relying on one model alone
• Can adapt better when traffic patterns shift
Attention Mechanisms
• Transformer-style models look at longer patterns in the data
• They help identify which signals matter most
• Strong option for large, multi-feature telemetry streams
Presenter: Mazen Alhassan
12 / 25

## Slide 13
ML for QoS Optimization
Using telemetry and predictions to keep service quality high
Presenter: Esam Mukbil
Reinforcement Learning
An agent tries actions and learns which routing or scheduling choices give better QoS.
Deep Q-Networks
Use the current network state to choose actions like rerouting, balancing load, or assigning bandwidth.
Multi-Objective Optimization
Helps balance trade-offs such as low delay, good throughput, and fairness at the same time.
Federated Learning
Lets different domains train shared models without sending all raw telemetry to one place.
Presenter: Esam Mukbil
13 / 25

## Slide 14
Performance & QoS: Main Lessons
What stood out most across the literature
Presenter: Esam Mukbil
1
Topology matters
GNNs usually beat plain time-series models when the shape of the network affects performance.
2
RL is powerful but risky
Reinforcement learning looks strong in simulations, but deployment is harder because bad actions can hurt live traffic.
3
Good data matters most
Missing or noisy telemetry can hurt prediction quality more than model choice.
4
Proactive beats reactive
Predicting trouble early is better than waiting for thresholds to fail after users are already affected.
Presenter: Esam Mukbil
14 / 25

## Slide 15
ML-Enhanced Network Telemetry Pipeline
A cleaner flow from data to action
Presenter: Mazen Alhassan
Collect
Devices export live network data
Store
Platforms organize and retain telemetry
Analyze
ML models detect patterns and predict issues
Act
Operators or automation respond faster
The pipeline matters because good telemetry architecture makes reliable ML and faster response possible.
Presenter: Mazen Alhassan
15 / 25

## Slide 16
PART 3
Pipeline, Industry & Conclusion
Presenters: Mazen Alhassan & Hashim Kshim
16 / 25

## Slide 17
Industry Example: Nokia
Showing what ML-driven telemetry looks like in practice
Presenter: Mazen Alhassan
Collect
Gather live broadband telemetry from many devices.
Analyze
Use ML to detect anomalies and estimate risk.
Act
Support faster troubleshooting and predictive maintenance.
What Nokia Is Trying To Do
Predict failures early | find unusual behavior automatically | estimate customer experience | forecast capacity needs | speed up troubleshooting
Presenter: Mazen Alhassan
17 / 25

## Slide 18
Case Study: Real-Time Anomaly Detection in Network Telemetry
Presenter: Mazen Alhassan
The Problem
• Telemetry streams massive time-series data (CPU, traffic, link utilization) from routers/servers in real time
• Operators cannot manually monitor everything — ML is needed to automatically flag abnormal patterns
• Challenge: detect anomalies in real time with low false positives, without large labeled datasets
The Study: AREP (Pekar et al., 2022)
• Uses an LSTM neural network to predict the next telemetry data point, then compares prediction to actual value
• If the difference exceeds a threshold, it flags an anomaly
• Key innovation: AREP auto-tunes its detection window and ageing coefficient — no manual parameter setup
• Offset compensation retrains the model when predictions start to drift
How AREP Works
Telemetry Stream
LSTM Prediction
Compare to Actual
Anomaly Score
Alert
Results
• Tested on the Numenta Anomaly Benchmark (NAB) — standard for streaming anomaly detection
• AREP outperformed predecessors (ReRe, Alter-Re²) on irregular telemetry patterns
• Follow-up study (Pekar et al., 2024): on periodic server farm data, simpler Bayesian Changepoint (F: 0.66) beat AREP (F: 0.20)
• Takeaway: LSTM excels on irregular patterns but struggles with highly periodic data — no single ML method wins everywhere
Presenter: Mazen Alhassan
18 / 25

## Slide 19
Case Study: Predicting Internet Traffic from Telemetry Data
Presenter: Mazen Alhassan
The Problem
• Operators need to predict future traffic volumes to avoid congestion and plan capacity
• Telemetry is collected by sampling SNMP MIB counters on router interfaces (e.g., every 5 min) — giving a time series of bits-per-second
• Traditional methods like ARIMA struggle with sudden spikes and complex patterns in real network traffic
The Study: ConvLSTMTransNet (Pekar et al., 2024)
• A hybrid deep learning model combining three architectures: CNN (local patterns), LSTM (time dependencies), and Transformer encoder (long-range relationships)
• Trained and tested on real ISP telemetry from high-speed 40 Gbps ports on a provider edge router, sampled at 5-min intervals via SNMP
• This is real Juniper Networks ISP telemetry — not synthetic data
Model Architecture
Telemetry Time Series
CNN Local Patterns
LSTM Time Deps
Transformer Long-Range
Traffic Prediction
Results
• Compared against three baselines: plain RNN, LSTM, and GRU
• ConvLSTMTransNet outperformed all three by ~10% better accuracy (MAE, RMSE, WAPE)
• Combining CNN + LSTM + Transformer captures both short-term spikes and long-term trends better than any single model
• Trade-off noted: more complex models need more compute and training time
Presenter: Mazen Alhassan
19 / 25

## Slide 20
Industry Example: Ericsson
Combining better data organization with automation
Presenter: Hashim Kshim
AI-Ready Data Mesh
Ericsson treats telemetry as a shared data product, not just raw logs. Teams manage domain pipelines with common standards, which improves data quality and makes telemetry easier for ML teams to use.
Transport Automation Controller (TAC)
Uses AI/ML to monitor transport performance, detect KPI anomalies, and support proactive capacity planning. Direction: closed-loop automation through detect, diagnose, and act workflows.
Key Industry Insight
Ericsson shows that good AI outcomes depend on strong telemetry and data foundations. Better data pipelines make network automation and prediction more realistic at scale.
Presenter: Hashim Kshim
20 / 25

## Slide 21
Emerging Trends: 6G & GenAI
Two trend groups that shape the future of telemetry
Presenter: Hashim Kshim
6G & Next-Gen Telemetry
Edge intelligence, digital twins, semantic telemetry, and AI-native design.
Generative AI & LLMs for Telemetry
Natural-language analytics, synthetic data, incident summaries, and foundation models.
Presenter: Hashim Kshim
21 / 25

## Slide 22
Open Challenges
Important problems that still need better solutions
Presenter: Hashim Kshim
Not enough labeled data
Real networks rarely provide clean examples of every failure or attack.
Scale and speed
Models must handle massive telemetry streams quickly enough to matter.
Explainability
Operators need to know why a model raised an alert before they trust it.
Concept drift
Normal traffic changes over time, so models can become outdated.
Generalization
A model that works well in one network may fail in another.
Privacy and security
Telemetry can contain sensitive information that must be protected.
Presenter: Hashim Kshim
22 / 25

## Slide 23
Conclusion & Key Takeaways
A cleaner final summary
Presenter: Hashim Kshim
1
Telemetry gives the raw picture
It tells us what the network is doing right now through streams of measurements and events.
2
ML helps turn data into decisions
It can find anomalies, predict future performance, and help improve QoS.
3
Industry is already using these ideas
Companies such as Nokia and Ericsson are building more automated, ML-driven telemetry systems.
4
The field is still growing
6G, digital twins, and generative AI may make telemetry smarter and easier to use.
5
The hardest part is deployment
Real-world success still depends on trustworthy models, good data, and systems that scale.
Presenter: Hashim Kshim
23 / 25

## Slide 24
Thank You!
Questions & Discussion
Abdul Rehman | Esam Mukbil | Hashim Kshim | Mazen Alhassan
NET3006A — Machine Learning for Network Telemetry
24 / 25

## Slide 25
References
Presenter: All Members
[1] Nokia, "Modern Broadband Network Telemetry," Nokia White Paper, 2024.
[2] Ericsson, "From data mess to AI-ready data mesh," Ericsson Blog, 2024.
[3] Ericsson, "Visualizing network performance: Transport Automation Controller with AI/ML at the helm," Ericsson, 2024.
[4] Z. Yuan et al., "iTeleScope: Softwarized Network Middle-Box for Real-Time Video Telemetry and Classification," IEEE/ACM Trans. Netw., 2023.
[5] A. Dogra et al., "6G Network Architecture: QoS Paradigms and Data Lifecycle Management for Next-Generation Networks," IEEE Commun. Surveys Tuts., 2024.
[6] S. Falkner et al., "Mobile Network Data Synthesis with Generative AI: Challenges and Solutions," IEEE Network, 2024.
[7] M. Boban et al., "Autonomous network operations: from reactive management to intent-driven optimization," Ericsson Technology Review, 2024.
[8] Ericsson, "Four ways generative AI is set to transform the telecom industry," Ericsson Blog, 2024.
[9] ATIS, "Advancing Generative AI Implementation in Telecommunications Networks," ATIS White Paper, 2024.
[10] R. Boutaba et al., "A comprehensive survey on machine learning for networking," ACM Comput. Surv., vol. 51, no. 5, 2018.
[11] P. Mishra et al., "A detailed investigation and analysis of using ML techniques for intrusion detection," IEEE Commun. Surveys Tuts., 2019.
[12] F. Tang et al., "A survey on machine learning for traffic classification," IEEE Trans. on Network and Service Management, 2022.
25 / 25